## Slide 2: LEVIN LAB PIRE ACTIVITIES Mehring/Levin/Kraikittikun
UPP Summer 2013 (Animals in Australia Biofilters and Wetlands)
  Summer sorter: Garfield Kwan
  ESYS Senior Thesis - Dianna Kraikittikun
Can animals improve the efficiency of bioretention systems?
(Review Manuscript In Prep: Mehring and Levin, Frontiers in Ecology and the Environment)
Animal mediation of phosphate availability:
Lab Experiment: Dec-Jan2014
Fe + P ;
Earthworms, Millipedes, Earthworms + Millipedes
Fe reducing microbes (Geobacter, Shewanella)
New Field Work: Monash/Melbourne Australia
Biofilter chronosequence: Infaunal Succession
Biofilter harvesting: Infaunal Consequences (Belinda Hatt)
Chironomid release of greenhouse gasses: Treatment Wetlands (P. Cook)

## Slide 3: Levin-Lab Biofilter/Wetland Questions
What are the dominant soil taxa and their lifestyles in biofilters? Treatment wetlands?
What factors influence faunal availability?
Age and size? Plant sp. & properties? Soil root and detrital organic matter?
What roles do animals play in water purification?
Vertical drainage: reduce clogging
Contaminant retention –
Direct reduction (or spread of pathogens)
Enhanced denitrification (in guts or via bioirrigation)
Enhance NO3 leaching, P mobilization, metal mobility
Metal accumulation
Indirect effects on plant growth, metal uptake etc.
Nutrient remineralization
Greenhouse gas emissions (CH4, N20) – through effects on soils and guts

## Slide 4: UPP 2013 – Biofilter Fauna
Chart: Richness
| Wicks | Lynbrook | Hereford
 | 3.75 | 5 | 2.7143
Chart: Abundance (individuals m-2)
| Entomobryomorpha | Poduromorpha | Isopoda | Amphipoda | Coleoptera | Diplura | Acari | Diplopoda | Oligochaeta | olig cocoon full | olig cocoon empty | Nematoda | Thysanoptera | Homoptera | Ostracoda | Chironomidae
Wicks | 763.9437 | 763.9437 | 0 | 0 | 0 | 0 | 381.9719 | 0 | 29793.8053 | 2928.451 | 254.6479 | 0 | 0 | 0 | 127.324 | 1782.5354
Lynbrook | 509.2958 | 1867.418 | 169.7653 | 0 | 509.2958 | 339.5305 | 1697.6527 | 169.7653 | 679.0611 | 0 | 339.5305 | 339.5305 | 0 | 0 | 0 | 0
Hereford | 24.2522 | 400.161 | 0 | 24.2522 | 60.6305 | 0 | 0 | 72.7565 | 8985.4334 | 2267.579 | 5844.7758 | 0 | 36.3783 | 60.6305 | 0 | 0
Low number of species
Oligochaetes dominate

## Slide 5: What are the dominant soil taxa and their lifestyles in biofilters?
Chart: Abundance (individuals m-2)
| Wicks | Hereford | Lynbrook
Oligochaeta | 29793.8053 | 8985.4334 | 679.0611
Acari | 381.9719 | 0 | 1697.6527
Poduromorpha | 763.9437 | 400.161 | 1867.418
Entomobryomorpha | 763.9437 | 24.2522 | 509.2958
Isopoda | 0 | 0 | 169.7653
Coleoptera | 0 | 60.6305 | 509.2958
Diplura | 0 | 0 | 339.5305
Diplopoda | 0 | 72.7565 | 169.7653
Nematoda | 0 | 0 | 339.5305
Thysanoptera | 0 | 36.3783 | 0
Homoptera | 0 | 60.6305 | 0
Amphipoda | 0 | 24.2522 | 0

## Slide 6: What are the dominant soil taxa and their lifestyles in biofilters?
Total densities (ind/m2):
Wicks – 33,486
Lynbrook Estate – 5,942 Hereford Road – 9,664

## Slide 7: What are the dominant soil taxa and their lifestyles in treatment wetlands?
Chart: 
| Oligochaete | Oligochaete coccoon | Chironmid | Chironmid pupa | Trichoptera | Platyhelminthes | Polychaeta
 | 19789.7341 | 4801.9208 | 14987.8133 | 15788.1334 | 1091.3456 | 72.7564 | 72.7564
Macrofauna Individuals m-2 (cores)
Total macrofaunal densities (ind /m2):
Edithvale – 19,047; Royal Garden 28,011; Hampton Park – 42, 271

## Slide 8: Wetland animals in sweep nets that were not detected in cores
Corixidae (water boatman)
Gambusia sp. (mosquitofish)
mosquito

## Slide 9: What are the dominant soil taxa and their lifestyles in treatment wetlands?
Meiofauna individuals m-2 (cores)
Chart: 
| Nematoda | Ostracoda | Copepoda
 | 50.8571 | 12.7143 | 1.7143

## Slide 10: Factors influencing faunal abundance in biofilters
Chart: % organic matter 45-300 µm
| 0.173061090647394 | 0.148686037985548 | 0.769751963993672 | 0.154855785762917 | 6.321930718482415 | 1.09758152206889 | 4.91746981129282 | 14.76776789224141 | 6.876853376943578 | 6.525227279231497 | 11.91624963057131 | 13.07961071547056 | 12.60412337425717 | 7.836101742071841
 | 0.36046 | 0.15509 | 0.58228 | 0.099561 | 0 | 0.056443 | 0.038456 | 1.1031 | 0.27335 | 0.71546 | 4.1715 | 2.5365 | 2.5606 | 2.9775
Chart: % cover rushes
| 20.0 | 10.0 | 45.0 | 0.0 | 12.5 | 0.0 | 0.0 | 7.5 | 0.0 | 0.0 | 65.0 | 40.0 | 75.0 | 75.0
 | 0.36046 | 0.15509 | 0.58228 | 0.099561 | 0 | 0.056443 | 0.038456 | 1.1031 | 0.27335 | 0.71546 | 4.1715 | 2.5365 | 2.5606 | 2.9775
Rush cover | OM. 45-300 um | Roots | Sedge cover | Max core depth
0.95 | 0.88 | 0.59 | 0.26 | 0.16
+ | + | - | + | +
Parameter relative importance weights (range 0-1)
Top model R2adjusted = 0.89
1. organic 45-300 µm 2. rush % cover 3. roots
(>2mm,0.3-2, 0.045-0.3 mm tested)