## Slide 1: QUANTIFYING ECOSYSTEM SERVICES PROVIDED BY HYPORHEIC EXCHANGE
Stanley B. Grant and Morvarid Azizian
Civil and Environmental Engineering, University of California Irvine & Infrastructure Engineering, University of Melbourne
Objectives
Present an analytical model of benthic exchange and reaction
Pumping of solute across bedforms
Advection-dominated mass transport
First-order reaction in sediment
Evaluate model
Compare to numerical solution
Derive solution for solute flux into the sediment
Application
Correlations for mass transfer coefficient
Trade-off between volume of water processed in the sediment and extent of reaction
streamline geometry
pressure head
velocity field
Elliot and Brooks Velocity Model
normalize by wave number
variable definitions
predicted concentration field
predicted concentration field (analytical)
Solution approach (neglect dispersion & diffusion)
Numerical simulation results
variable definitions
flux into sediment bed
mass-transfer-limited flux
Numerical approach (governing equations)
variable definitions
advection/dispersion equation
dispersion tensor
predicted concentration field (numerical)
Numerical and analytical solutions near-identical
Numerical simulation carried out with COMSOL
Mechanical dispersion & molecular diff. negligible
Dirichlet b.c. at surface causes gradient artifact
Applications
Analytical model supports use of mass transfer coefficient
Flux ~ conc. diff. in upwelling & downwelling zones
Mass transfer coefficient = downwelling velocity
Ecosystem services
Flux into sediment = mass removal in sediment
Mass removal in sediment = ecosystem service (N, P, C processing; CEC removal)
Model identifies trade-off between volume of water processed by hyporheic zone and extent of reaction in sediment (hard to optimize both)
Acknowledgements
Funding by the National Science Foundation Partnerships for International Research and Education (PIRE) Award No. OISE-1243543. A huge THANK YOU to Keith Stolzenbach (UCLA), Megan Rippy (UCI), Mike Stewardson (UoM), and Perran Cook (Monash Univ).